Motion control with EPICS
Torsten Bögershausen
Motion Control and Automation Group
www.europeanspallationsource.se

---
epics-modules/motor
- EPICS has a complete package for motors:
  - record(motor)
  - Generic driver (model 3)
  - Specific drivers for different controllers
- https://github.com/epics-modules/motor
- Many changes/improvements:
  github.com/europeanspallationsource/motor

---
5 important things in motorRecord
One motor:

---
5 important things in record
- Which position should the motor be ?
- At which position is the motor ?
- Status, alarms, problems ?
- What is the motor doing ?
- Stop the motor

---
5 most important fields
- EPICS record name: e.g. IOC:m1
- Fields belonging to the record:
  - Where should the motor be ? IOC:m1.VAL
  - Where is the motor ? IOC:m1.RBV
  - Alarms :
       IOC:m1.STAT IOC:m1.SEVR
  - Stop the motor IOC:m1.STOP

---
More important fields
Read only fields:
- IOC:m1.MOVN Motor moving
- IOC:m1.DMOV Movement done
        (After backlash and delay)
- IOC:m1.MISS Position not reached
- IOC:m1.LVIO (Soft) Limit Violation
- IOC:m1.HLS, LLS High/Low
        limit switch activated

---
Extra PV
The IOC:m1-MsgTxt PV:
Shows additional information:
’E: Controller error 4650’
’Homing’

---
Move to a position
Write fields:
Optional:
- IOC:m1.VELO Velocity
- IOC:m1.ACCL Acceleration time (sec)
or
- IOC:m1.ACCS Acceleration (mm/sec²)
finally:
IOC:m1.VAL Target position

---
Move with constant velocity
Write fields:
- IOC:m1.JVEL Velocity
- IOC:m1.JAR Acceleration (mm/sec²)
- IOC:m1.JOGF Move forwad
- IOC:m1.JOGR Move reverse

---
Homing
- Write fields:
  - IOC:m1.HOMF Home (forward)
  - IOC:m1.HOMR Home (reverse)
- (Today, both do the same)
  All homing is configured in TwinCAT
  (today nearly all).

---
EPICS Record Alarms
- All EPICS records have 2 fields:
  STAT
  SEVR
- STAT == 0 means ”no alarm”
- SEVR is valid when STAT != 0.
  E.g. distinguish between Major/Minor

---
The STAT field
EPICS base: enum, 20 values.
0 == epicsAlarmNone
(read, write)
(hihi, high, lolo, low)
7 == epicsAlarmState
9 == epicsAlarmCom
14 == epicsAlarmLink
17 == epicsAlarmUDF

---
The SEVR field
EPICS Base, enum, 4 values.
0 == epicsSevNone
1 == epicsSevMinor
2 == epicsSevMajor
3 == epicsSevInvalid

---
STAT + SEVR
Combinations
AlarmUDF, SevInvalid
AlarmHigh, SevMajor/SevMinor/SevNone
AlarmLow, SevMajor/SevMinor/SevNone
AlarmCom, SevInvalid
AlarmState, SevMajor/SevMinor/SevNone

---
Alarms, what, when
- AlarmUDF
  (TCP/IP) connection never established
- AlarmCom:
  (TCP/IP) connection lost
- AlarmState:
  ”motor problem”
- AlarmHigh,Low:
  Soft/hard limit (See HLSV)
- AlarmState:
  MISS (See MISV)

---
End of motor
- End of EPICS motor
- Spontanous questions ?
- Over to epics-twincat-ads