## Slide 1
EPICS module for PMAC
Control
Alan Greer

## Slide 2
EPICS module for PMAC
Control
Alan Greer
Gary Yendell

## Slide 3
Current Control of PMAC
3 EPICS driver modules required
  tpmac – includes asyn type 2 and 3 control code for raw motors
  pmacCoord – includes asyn type 2 control code for CS axes
  pmacUtil – provides utility records for PMAC status
Stream device required for additional messages
Multiple points of control, messages sent to PMAC from all of the modules
Simple moves supported but many features of PMAC are not utilised

## Slide 4
Goals of upgrading PMAC modules
Upgrade the driver to Asyn model 3
Combine all control code into a single module
Simplify communications, cut down traffic
Support changing Coordinate Systems on board the PMAC
Support model 3 trajectory scan interface
Maintain backwards compatibility

## Slide 5
EPICS pmac module
https://github.com/dls-controls/pmac
Replacement for tpmac, pmacCoord and pmacUtil.

## Slide 6
Features of pmac module
Message Broker
Coordinate System Support
Coordinate System Configurations
Trajectory Scanning

## Slide 7
Features: Message Broker (1/5)
3 Polling loops for variables (slow, medium and fast)
  Fast loop polled at 1Hz when no motors are moving and 10Hz otherwise
  Fast loop rate can be set
  Medium loop polled at 1Hz
  Slow loop polled at 0.1Hz
Variables combined into single large messages to cut down message overhead and traffic

## Slide 8
Features: Message Broker (2/5)
Variables added to the loops by using special Asyn parameter names in record database
PMAC_VDF_ Variable (V) of double (D) type added to the fast (F) loop
PMAC_VIM_ Variable (V) of integer (I) type added to the medium (M) loop
PMAC_VHS_ Variable (V) of hex (H) type added to the slow (S) loop

## Slide 9
Features: Message Broker (3/5)
Interested classes register for callbacks
  pmacController
  pmacCSController
  pmacAxis
  pmacCSAxis
Reduces number of threads and provides better control of message sending to the PMAC

## Slide 10
Features: Message Broker (4/5)
Statistics recorded to monitor traffic

## Slide 11
Features: Message Broker (5/5)
Improved debugging
Report contents of all monitored values at any time

## Slide 12: Features: Coordinate Systems
Asyn model 3 CS controller and axis classes
Standard CS status provided as Asyn parameters
Debug output available for individual axes
Currently assigned coordinate systems available for each motor (Asyn parameters)
Kinematics available (Asyn parameters)
Communication to PMAC through the broker

## Slide 13: Features: Coordinate System Configuration (WIP)
Coordinate systems assignments can be specified during IOC runtime
Coordinate system assignments can be saved as a configuration
Saved coordinate system configurations can be loaded

## Slide 14: Features: Trajectory Scan (1/10)
Generic trajectory scan implementation provided
Double buffer allocated on board the PMAC

## Slide 15: Features: Trajectory Scan (2/10)
As PMAC hardware reads from buffer A, buffer B is free to be filled by the pmac driver
When PMAC hardware reaches the end of buffer A, it switches to buffer B and A becomes free to be filled by the pmac driver

## Slide 16: Features: Trajectory Scan (3/10)
Buffers are filled using writes to memory locations – no PMAC message corruption (no open buffers)
Buffer size and location can be customised per PMAC
Driver reads the configuration from the PMAC, no special setup required
Motor record trajectory scan interface supported with additional records for user modes

## Slide 17: Features: Trajectory Scan (4/10)
Only 1 coordinate system can be trajectory scanned at any time
Any coordinate system axes can be included (or ignored) for a trajectory scan

## Slide 18: Features: Trajectory Scan (5/10)
Scans are executed using PVT mode on the PMAC
User routines can be executed during moves
Driver reads back the current scan status
Positions and delta times are supplied, velocities are calculated in one of three ways
  Velocity 1: previous to current
  Velocity 2: previous to next
  Velocity 3: current to next

## Slide 19: Features: Trajectory Scan (6/10)
  Velocity Mode:

## Slide 20: Features: Trajectory Scan (7/10)
  Velocity Mode:

## Slide 21: Features: Trajectory Scan (8/10)
  Velocity Mode:

## Slide 22: Features: Trajectory Scan (9/10)

## Slide 23: Features: Trajectory Scan (10/10)
Motion program and associated Python test scripts supplied with the module

## Slide 24: Thank You
Any Questions?