Connecting EPICS to TwinCAT
Torsten Bögershausen
SW Engineer
www.europeanspallationsource.se
2024-04-16
[Speaker Notes: Some good development done @ ESS, worth to mention]

---
Epics com module
- ”first generation”
- Presented at the EPICS meeting 2015 at FRIB. Dead link:
  http://www.frib.msu.edu/misc/epics2015/index.htm
- 2nd generation much more advanced:
  (indexer,timestamping, EPICS alarms from PLC)
- New code for TwinCAT and EPICS

---
Connections to TwinCAT
Connections to TwinCAT
FB_DriveVirtual
Motor
Encoder, switches
PLC
Motion
Ethercat master
TwinCAT
real time
 kernel
winsock
COM
OPC
EPICS IOC
ADS
Control network: EPICS channel access, pvaccess
[Speaker Notes: - IOC should be run under defined Linux Clean separtion between EPICS and non EPICS - Can cut the wire: simulate the motor + MCU - 2 different people look from different sides at the same interface: - 2 brains give better code - Can upgrade both parts independently]

---
EPICS Com Module
EPICS Com Module
EPICS Com
Module
(realtime under
  TwinCAT)
ADS Router
FB_DriveVirtual
Motor
Encoder, switches
PLC
Motion
Ethercat master
TwinCAT
real time
 kernel
winsock
EPICS IOC

---
ASCII data
ASCII data
Low level debugging
$ telnet 192.168.88.48 5000
Main.M1.bBusy?;\r\n
0;\r\n
EPICS TwinCAT
IOC
Stream-
Device
TwinCAT
System
“Main.M1.fPosition=10.0;\n”
“OK;\n”

---
EPICS – PLC communication
- ”Move absolute” to position 200
- Main.M1.bExecute=0;
  Main.M1.nCommand=3;
  Main.M1.nCmdData=0;
  Main.M1.fPosition=200.0;
  Main.M1.bExecute=1
- (Not shown: fVelocity,fAcceleration,
          fDecelaration)
- (Not shown: ADSPORT=851)

---
EPICS from python
- Python: ”Move absolute” to position 200
- Import pyepics
- m1 = ”IOC:m1”
- Position = 200
- caput(m1, position)
  And when is the motor done ?

---
Client EPICS MR & wait
- m1 = ”LabS-ESSIIP:MC-MCU-01:m1”
- Position = 200
- caput(m1, position, wait=true)
  #And now the movement is done

---
Client EPICS MR & STAT field
- #And now the movement is done
- stat = caget(m1 + '.STAT')
  if (stat != 0):
    # Error handling
    # To be discussed
    # with ”Users”

---
Move & monitor a motor
Move & monitor a motor
(done on a simulator, Mac or raspi)
- camonitor IOC:m1.RBV IOC:m1.DMOV
- IOC:m1.RBV 2016-02-02 10:58:16.157350 24.87
- IOC:m1.DMOV 2016-02-02 10:58:16.658745 1
- IOC:m1.DMOV 2016-02-02 10:58:16.658745 0
- IOC:m1.RBV 2016-02-02 10:58:30.124368 49.86
- IOC:m1.RBV 2016-02-02 10:58:31.138087 60.06
- IOC:m1.DMOV 2016-02-02 10:58:31.639072 1
- caput IOC:m1.VAL 60.1
- Old : IOC:m1.VAL 24.9
- New : IOC:m1.VAL 60.1
#Notes:
#caput: Channel access put
#camonitor: Channel access monitor
#IOC:m1..DMOV: Field “done moving”
#IOC:m1.RBV: Field Read back value

---
epics-twincat-ads
- Now comes the ”1.5 generation”
- Used for this demo
- In production at ESS, SLAC

---
ADS
2015:
Code from Beckhoff to ”talk” ADS from
Windows, Linux, MacOS
- https://github.com/Beckhoff/ADS.git
- Yeah!
- https://github.com/europeanspallationsource/epics-twincat-ads

---
EPICS ads Module
ADS Router
FB_DriveVirtual
Motor
Encoder, switches
PLC
Motion
Ethercat master
TwinCAT
real time
 kernel
  asyn
  ads
ethercatmc
motor

---
commissioning
Over to commissioning

---
commissioning
- From communication to commissioning
  MotorRecord approach:
  ”dump” controller card:
  All configuration i EPICS
- Modern controller approach:
  All configuration inside the controller
- ESS:
  commission the controller
  read data intoEPICS

---
commissioning
When we commission a crate these values are
configured:
- Scaling/Resolution (mm/rev, steps/rev)
- Maximum velocity
- Default velocities (positioning, jog, homing)
- Default acceleration, jerk
- Soft limits
- In target position monitor (deadband)
- Many more

---
Config parameters from TwinCAT into EPICS

---
Commission MCU → motorRecord
Read data from MCU into Record:
out=ADSPORT=501/.ADR.16#4001,16#16,8,5?;…
in=1.0e-1;2.0e-2;...
rdbd=0.100000, rdbd_tim=0.020000 rdbd_en=1
IOC:m1 enforceMinRetryDeadband...cfg_rdbd=0.100000
Why important:
- When is a movement ”completet” ?
- Movements with smaller distances are ”ignored”

---
That’s it
- Thanks – for listening
- Time for questions